## Slide 1: Gemmini Exploration Files
21/09/2022

## Slide 2: Environment
Chipyard is an open-source SoC development platform launched by UC Berkeley
Chipyard provides many components for building SoC around the RISC-V CPU and also provides many environments for testing and development
Among the components of Chipyard, the CPU based on the RISC-V instruction set includes: Rocket core, Berkeley Out-of-Order Machine (BOOM), CVA6, and Ibex core

## Slide 3: Environment
In terms of hardware accelerators, Chipyard supports: Hwacha, Gemmini, SHA3 and NVDLA and other hardware accelerators with different purposes
System components including Icenet, Sifive-blocks, Analog Widget Library (AWL), testchipip, etc can be used during testing
  These IPs are open-source and can be used at no additional cost

## Slide 4: Environment
Development tools and toolchains provided include Constructing Hardware in a Scala Embedded Language (Chisel), A Flexible Intermediate Representation for RTL (FIRRTL), Bartools, Dsptools, Dromajo, riscv-tools, esp-tools, etc.

## Slide 5: Environment
Simulators provided include Spike (RISC-V ISA Simulator), Verilator (open-source), VCS (license needed ), and the cloud-based FPGA simulation provided by the University of Berkeley Device (FireSim)
Chipyard also supports two VLSI design methods: FPGA Prototyping and ASIC

## Slide 6: Chipyard Design Flow
Select the chipyard open-source CPU, the design expressed by Chisel, the external interface, the external devices, cache memory, AI hardware accelerator
After the hardware configuration the Chisel is replaced with Verilog through FIRRTL (a hardware compiler)
RTL simulation tools such as Verilator and VCS can be used for simulation or FPGA simulation can be run on the cloud system established by the University of Berkeley

## Slide 7: Chisel
Chisel is an open-source high-level HDL embedded in Scala developed by the University of Berkeley
Chisel is mainly used to describe digital circuits in RTL and some highly parameterized circuits
Chisel adds the syntax of constructing hardware to Scala language, which provides hardware circuit designers with powerful functions similar to the current mainstream software programming languages such as Python, C, etc.
Through the hardware compiler, it can generate Synthetic Verilog circuit
The use of parameters makes the design more intuitive and easy
The University of Berkeley used Chisel to design a CPU based on the RISC-V instruction set
To put it simply, Chisel can be understood as a Verilog generator (requires the hardware compiler FIRRTL), which can quickly and efficiently develop hardware designs by using Scala syntax

## Slide 8: FIRRTL
FIRRTL is a hardware compiler based on Chisel: Its main function is to compile Chisel into Verilog
When FIRRTL works as a hardware compiler, it will optimize the circuit through algorithms, resource sharing, reuse of specific modules, and reduction of unnecessary registers, etc.
It will also report syntax error of the Chisel code
FIRRTL also supports adding specific rules or conditions in the hardware compiler, so that FIRRTL can better meet the circuit conversion mode needed

## Slide 9: Rocketchip Generator
Tiles: unit of replication for a core
  CPU
  L1 Caches
  Page Table Walker (PTW)
L2 banks
  Receive memory requests
FrontBus
  Connects to DMA devices
ControlBus
  Connects to core complex devices
PeripheryBus
  Connects to other devices
SystemBus
  Ties everything together

## Slide 10: Rocket Core
Each Rocket core is grouped with:
  A page-table walker
  L1 instruction cache
  L1 data cache
The Rocket core
  First open-source RISC-V CPU
  In order, single issue RV64GC core
  64-bit 5-stage single-issue in-order pipeline
  Design minimizes impact of long clock-to-output delays of compiler-generated RAMs

## Slide 11: Gemmini Framework Analysis
The core of the Gemmini accelerator is a circuit composed of a Systolic Array that performs matrix multiplication, and is also a part of the Chipyard ecosystem
Gemmini is implemented through the Chisel HDL
The circuit can realize the acceleration of matrix multiplication, convolution operation and other operations that require a lot of CPU resources in the form of data flow
Currently, the data flow methods supported by Gemmini include Weight Stationary (WS) and Output Stationary (OS)

## Slide 12: Gemmini Framework Analysis
Gemmini is a Rocket Custom Coprocessor Interface (RoCC) accelerator using RISC-V custom instructions
  Using Rocket or BOOM core, the RoCC interface issue instruction to and from Gemmini
A Direct Memory Access (DMA) controller to move the data to and from Gemmini
Gemmini hardware supports: DMA Controller, Scratchpad, Activation Function Unit, Scaling Function Unit, Transposer, Systolic Array etc.

## Slide 13: Installing Chipyard and Gemmini Tools
Run the steps to install Chipyard and Gemmini tools
  $ git clone https://github.com/ucb-bar/chipyard.git
  $ cd chipyard
  $ git checkout 117624d8eea27bafd613eec09e9b9b3e31239e08
  $ ./scripts/init-submodules-no-riscv-tools.sh
  $ ./scripts/build-toolchains.sh esp-tools
  $ source env.sh
  $ cd generators/gemmini
  $ git fetch && git checkout v0.6.4
  $ git submodule update
  $ cd -
  $ cd toolchains/esp-tools/riscv-isa-sim/build
  $ git fetch && git checkout 090e82c473fd28b4eb2011ffcd771ead6076faab
  $ make && make install

## Slide 14: Installing Chipyard and Gemmini Tools
Inside the Chipyard directory

## Slide 15: Workflow
This work explored the effects of several configuration parameters of the Gemmini accelerator on both performance and hardware resource utilization by using a development framework that is made up of a combination of both open-source and proprietary tools
The flow is organized into three interconnected categories which include
  The Gemmini SoC RTL code Generation Flow
  The Software Code Compilation Flow
  Gemmini RTL Code Synthesis Flow

## Slide 16: Workflow
This section details the workflows giving the steps involved and the tools used in each step

## Slide 17: SoC RTL Generation (L1Cache)
Config file location

## Slide 18: SoC RTL Generation (Rocket Core)
Config file location

## Slide 19: SoC RTL Generation (Rocket Core)
Config file location
Different Rocket cores
Config | Big Core | Med Core | Small Core | Tiny Core
Datawidth | 64 | 64 | 64 | 32
FPU | Available | None | None | None
Instruction Cache | 16KB | 4KB | 4KB | 4KB
Data Cache | 16KB | 4KB | 4KB | 4KB
Cache Mapping | 4-way Set Associative | Direct Mapping | Direct Mapping | Direct Mapping

## Slide 20: SoC RTL Generation (Gemmini)
Config file location

## Slide 21: SoC RTL Generation (Gemmini)
Config file location

## Slide 22: SoC RTL Generation (Gemmini)
Config file location

## Slide 23: Gemmini Build Outputs
Gemmini build outputs

## Slide 24: Gemmini Hardware/Cycle-Accurate Simulators
Run the instructions below to build a cycle-accurate Gemmini simulator using Verilator
  cd chipyard/generators/gemmini
  ./scripts/build-verilator.sh
After running this, in addition to the cycle-accurate simulator, you will be able to find the Verilog description of your SoC in generated-src/

## Slide 25: View Generated Verilog
Some Generated Verilog files for Gemmini SoC

## Slide 26: View Generated Verilog
Modules inside Gemmini

## Slide 27: Configuration Parameters
The figure illustrates the configuration parameters selected for generating the Gemmini accelerators for this work and the overall architecture for simulating the Gemmini SoC

## Slide 28: Gemmini Modules (Overall)
Gemmini Modules

## Slide 29: The RoCC Interface
The Rocket Custom Coprocessor (RoCC) Interface

## Slide 30: RoCC Instruction Format
RoCC instruction format

## Slide 31: Gemmini Assembly-level ISA
Gemmini assembly-level ISA

## Slide 32: Gemmini Assembly-level ISA
Data movement

## Slide 33: Gemmini Assembly-level ISA
Configuration

## Slide 34: Gemmini Assembly-level ISA
Configuration

## Slide 35: Gemmini Modules (LoopConv)
The LoopConv module is responsible for unrolling large convolutions to fit the systolic dimension of DIMDIM
It consists of modules such as LoopConvLdBias, LoopConvLdWeight, and LoopConvLdInput for signifying instructions for the convolution operation bias, weight, and input respectively
The LoopConvExecute and LoopConvst module are instructions for executing the convolution operation and storing results respectively

## Slide 36: Gemmini Modules (LoopMatmul)
The LoopMatmul module is responsible for unrolling large matrix multiplications (matmuls) to fit the systolic dimension of DIMDIM
In the module the LoopMatmulLdA, LoopMat-mulLdB, and LoopMatmulLdD specify the loading of matrix A, B, and D respectively while the LoopMatmulExecute module generates commands for the matrix multiplication
The LoopMatmulStC generates commands for storing the results of matrix C

## Slide 37: Gemmini Modules (Load/Store Controller)
The LoadController and StoreController are similar in design and are responsible for instructions that move data from the DRAM to the Gemmini Scratchpad and from Scratchpad to the DRAM respectively
The LoadController connects to the scratchpad DMA read interface while the StoreController connects to the scratchpad DMA write interface
Both controllers use a Finite State Machine (FSM) with three states including waiting_for_cmd, sending_rows, and waiting_for_dma_req_ready states for controlling their running modes

## Slide 38: Gemmini Modules (im2col)
When the Gemmini accelerator is configured to have an im2col module, the interface connects and receives instructions from the ExecuteController module and also reads data from the SRAM read interface of the scratchpad module
The read data is then fed to the ExecuteController module
The im2col module is an address generator that uses an FSM to make sure that the PEs inside the systolic array of the ExecuteController are used as much as possible
The states in the im2col FSM include nothing_to_do, waiting_for_im2col, preparing_im2col, and im2col_done

## Slide 39: Gemmini Modules (ExecuteController)
The controller connects to the im2col interface and SRAM interfaces of the scratchpad
The MultiHeadedQueue_1 module is a buffer that separates the instructions into commands for the Scratchpad module and the MeshWithDelays module
The instructions or commands for the scratchpad module are sent to extract data from the SRAMs
The commands for the MeshWithDelays are first buffered in the Queue_61 module before being sent to control the systolic array and other components in the module

## Slide 40: Gemmini Modules (MeshWithDelay)
The MeshWithDelays consists of modules such as the Mesh and AlwaysOutTransposer
The AlwaysOutTransposer is used to transpose a matrix before it enters the MeshWithDelays module
The AlwaysOutTransposer is implemented as a systolic array with configurable DIMDIM PEs

## Slide 41: Gemmini Modules (Mesh)
The module implements the systolic array of the Gemmini accelerator with configurable mesh rows and mesh columns
There are delay registers at each mesh output to enable each input from one matrix to arrive at the same time as the input of another matrix before multiplication
The PEs can also be configured to employ different dataflows such as OS or WS or both as shown in the figure

## Slide 42: Gemmini Modules (Scratchpad)
The scratchpad module is responsible for storing data that is generated during the matrix multiplication or convolution operation
It consists of input/output (IO) interfaces including spad_io_tlb (connects to the FrontTLB module), spad_auto_id (connects to the L2cache/DRAM), spad_io_dma_read/write (connects to DMA), spad_io_sram_read/write (connects to the ScratchpadBank), and spad_io_acc_read/write (connects to the AccumulatorMem)

## Slide 43: Gemmini Modules (ScratchpadBank)
The Figure shows the arrangement of the ScratchpadBank in the Scratchpad module which is made up of simple SRAMs
The number of banks is configurable but usually consists of four banks for storing matrices A, B, D, and C
Each bank has a default data width of 8 and a depth of DIM

## Slide 44: Gemmini Modules (AccumulatorMem)
The module is configurable but the default consists of two accumulators for storing the intermediate or final results of the matrix multiplication or convolution operation
The data width of each accumulator is a default value of 32 while the depth is DIM4
In addition to the SRAMs, the accumulators have a set of adders located in the AccPipeShared of the scratchpad module
They also have an internal scaler for transforming the 32-bit data width into 8-bit data width

## Slide 45: Software Code Compilation (GEMM)
The Gemmini hardware accelerator can be controlled in several ways
The control or programming of the Gemmini accelerator can be achieved at three different levels including:
  High-level programming of compiling ONNX models
  Mid-level programming using kernel libraries
  Low-level programming using assembly or direct machine configuration
To investigate the performance of GEMM on various configurations of the Gemmini accelerator, this work selected the mid-level programming of the accelerator

## Slide 46: Software Code Compilation (GEMM)
This work compiles bare-metal matrix multiplication programs that can be executed in the Gemmini hardware or the Rocket CPU core
The programs include the tiled_matmul_os.c for the OS dataflow option and tiled_matmul_ws.c for the WS dataflow option
A section of the tiled_matmul_os.c file is shown in the Figure

## Slide 47: Software Code Compilation (GEMM)
The program starts by initializing the matrices with random values before calling the full_matmul function for the execution of matrix multiplication on the Rocket CPU
The program then calls the tiled_matmul_auto function for the execution of matrix multiplication on the Gemmini accelerator
The tiled_matmul_auto function is located in the gemmini.h header file which was generated together with the Gemmini SoC Verilog files

## Slide 48: Software Code Compilation (GEMM)
The tiled_matmul_auto function runs matrix multiplication of dimensions that are higher than the systolic array by automatically calculating the tiling factors
The function then calls the tiled_matmul function with hardcoded tiling parameters which subsequently calls the tiled_matmul_outer function

## Slide 49: Software Code Compilation (GEMM)
The tiled_matmul_outer makes a series of configuration function calls including
  gemmini_extended3_config_ld: for moving matrix A, B, and D from DRAM to the Scratchpad
  gemmini_extended_config_st: for moving data from the Scratchpad to the DRAM
  gemmini_extended_config_ex: for executing the matrix multiplication in the systolic array of the ExecuteController module

## Slide 50: Software Code Compilation (GEMM)
Each of the configuration functions is arranged into the RoCCommand format and is transferred to the Gemmini accelerator through the RoCC interface

## Slide 51: Software Code Compilation (GEMM)
The RISC-V compiler (riscv64-unknown-elf-gcc version) is used to compile the tile_matmul_os.c and tiled_matmul_ws.c programs together with a linker file that points to the base address of the instruction memory

## Slide 52: Software Code Compilation (GEMM)
Executable (.exe) files are generated and converted to hexadecimal files (.hex) tiled_matmul_os.hex and tiled_matmul_ws.hex using the SiFive elf2hex program
The Verilator simulator loads the hexadecimal files into the designated location of the DRAM simulation module which prompts the Rocket CPU to begin executing instruc-tions starting from the base address
The simulator reports the performance of executing the matrix operations on both the Rocket CPU core and the Gemmini accelerators for comparison

## Slide 53: Gemmini 2x2 Matrix Multiplication Cycles
Performance Gemmini speedup relative to Rocket CPU
  Above 1 mean speedup and below 1 means slowdown

## Slide 54: Gemmini 8x8 Matrix Multiplication Cycles
Performance Gemmini speedup relative to Rocket CPU
  Above 1 mean speedup and below 1 means slowdown

## Slide 55: Gemmini 16x16 Matrix Multiplication Cycles
Performance Gemmini speedup relative to Rocket CPU
  Above 1 mean speedup and below 1 means slowdown

## Slide 56: Gemmini 32x32 Matrix Multiplication Cycles
Performance Gemmini speedup relative to Rocket CPU
  Above 1 mean speedup and below 1 means slowdown

## Slide 57: Gemmini 128x128 Matrix Multiplication Cycles
Performance Gemmini speedup relative to Rocket CPU
  Above 1 mean speedup and below 1 means slowdown

## Slide 58: Gemmini RTL Synthesis
The Verilog files of the Gemmini accelerators are synthesized using the commercial tool Vivado v2020.2
Four Gemmini accelerators are generated based on the systolic array size which includes 8  8, 16  16, 32  32, and 64  64 for comparison
Each of the accelerators has an option for including an im2col module or not
This work synthesized each of the Gemmini accelerators using the Virtex UltraScale+ XCVU19P-FSVA3824-1-E FPGA device
The synthesis report of each Gemmini accelerator produced the resources occupied, the maximum frequency, and the power consumption

## Slide 59: Gemmini RTL Synthesis
Gemmini hardware resource consumption

## Slide 60: Gemmini RTL Synthesis
Gemmini modules CLB LUT usage

## Slide 61: Gemmini Performance-Per-Area Analysis
The performance-per-area metric estimates the performance in terms of the execution time of various matrix dimensions on the generated Gemmini hardware architectures
It also estimates how each dataflow option makes use of the available hardware resources
The metric for a particular Gemmini accelerator is calculated as the ratio of the total speedup of the accelerator and the total number of CLB LUTs consumed
The speedup of a Gemmini accelerator is the ratio of the total execution time of all the GEMM operations on the accelerator and the Rocket CPU core

## Slide 62: Gemmini Performance-Per-Area Analysis
The Figure illustrates the performance-per-area of each Gemmini configuration as well as the performance speedups relative to the Rocket CPU